## Slide 1
Twin Cities
ANSYS® User Meeting
May 2015
Workbench v16 Update

## Slide 2: Agenda
Usability Enhancements
Adaptive Meshing
Weld Connections
Spaceclaim
Material Modeling Improvements
V15 reminders

## Slide 3: Moore’s Law
Simulation is increasingly underutilized!

## Slide 4: Analyst vs Advocate
Analyst
Get a Project
Work on the Project
Document the Results
Submit the Project
Advocate
Find Opportunities
Scope Projects
Direct the Analysis
Quantify Savings

## Slide 5: So what’s the difference?
Analyst
Unknown Value
40 hours Impact on Profits
Advocate
Valued Resource
Impact Multiplies
With more projects, whose expertise can you leverage?

## Slide 6: Use Epsilon as a Resource!
Design
Initial Analysis
Parametric Studies
Prototype
Redesign
Failure Modes
Sustain
Design Improvements
Reduce Costs

## Slide 7: What’s the Next Step?
Let’s get an NDA in place
  Just a phone call away
Discover Opportunities for Simulation
  Epsilon has a proven approach
Become a Champion of FEA
  Promote FEA as a necessity

## Slide 8: Usability Enhancements

## Slide 9: Folders
Parts, connections, boundary conditions, etc. can be organized into groups
Easily suppress whole groups without hunting for each item

## Slide 10: Node/Element Numbers
Display Node/Element numbers through “Annotation Preferences”
Show specific range of node/elements on the model if needed.

## Slide 11: Sub-Assemblies
Improved assembly management
  Can import more details from sub-models
  Improved detail management from folders
  “Preview Assembled Geometry” available
From ANSYS V16 Release Notes
From ANSYS Release Notes

## Slide 12: Face
Now you can split faces using planes and surfaces!

## Slide 13: Detach and Body Repair

## Slide 14: Vector Plotting controls
Vector Plotting allows suppression of principals

## Slide 15: Analysis Options
Tabular participation factor data for modal analyses
Results Option: set default for calculating time history
Can now plot stresses and strains for line bodies

## Slide 16: Misc.
Explode!
From ANSYS Release Notes

## Slide 17: Misc.
Can open Mechanical in read-only mode (avoids tying up license)
Filter Tree Based on Visible Bodies
Selection Information tells you distance between selected items
From ANSYS V16 Release Notes

## Slide 18: Misc.
Thermal Fluid Line Bodies: Import pipe volumes as line bodies to model thermal fluid flow
Image courtesy of PADT

## Slide 19: Misc.
Buckling: Now includes nonlinear effects, renamed Eigenvalue Buckling
  Incremental loads may now be added after static pre-stress
  Joints now supported in linear buckling
From ANSYS Release Notes

## Slide 20: Misc.
Distributed Mass
  Paint bodies, or surfaces with specified mass
Element Orientation—Use surface/edge guides
  Can adjust normals within Mechanical – but operates on entire body
Joint Element Control – define elements used in joints
  Contact or MPC184’s
Solver Pivot Checking – continue solving when underconstraint detected
  V15 became more sensitive to pivot errors
  V16 let’s us better ignore these errors
  See PIVCHECK MAPDL command)

## Slide 21: Misc.
IGES Import Instancing
  Can reuse meshing for instanced bodies, for example
DM – Upgrade Feature Version
  Can choose whether to update legacy .agdb’s
DM – sort parts alphabetically
Geometry attachment up to 2x faster
Multi-threaded (parallel CPU) contact detection

## Slide 22: Meshing

## Slide 23: Mesh Connections
ANSYS inc. continues trend avoiding shared topology.
This trend exists from WB inception.
Also note Spaceclaim alongside DM info.
From ANSYS Release Notes

## Slide 24: Mesh Connections
Connect parts/bodies in ANSYS by selecting the common point/edge/face between the two.
Allows for greater control of what is/isn’t connected
Connections can be “automated” similar to contacts
Large number of connections fail in our test cases

## Slide 25: Node Merging
Connect nodes between parts/bodies in ANSYS by selecting the common points/edges/faces.
  Like NUMMRG command in MAPDL
Allows for tolerance control between present node connections within the model

## Slide 26: What’s the Difference?!?
Mesh Connection:
  Mesh connection will move the nodes of the slave geometry to match the master geometry. Both bodies will share common nodes between the two.
Node Merge:
  Node merges will merge any nodes that are within the set tolerance. Small tolerances merge nodes on top of each other—large tolerances forces nodes to merge over a larger area.
Tolerance: 1e-5, Nodes Merged: 2
Tolerance: .25, Nodes Merged: 25

## Slide 27: Node Moving

## Slide 28: Display Element Quality
Display the mesh quality under “Mesh Details”
Quick and easy way to look at the effects of mesh connection/node merging/node moving
Uses combination of previous element quality viewing options

## Slide 29: Adaptive Remeshing
New feature for nonlinear, large deflection analyses: “Nonlinear Adaptive Region”
Intended to ressolve convergence issues with high deformation load cases, esp. elastomers
Extending trend from earlier “rezoning”
  previously only in MAPDL
Still has lots of caveats
  Commercial application is still narrow/costly
Notes: Escape: equivalent to New Selection (if button is not grayed out; also accessible via the Selection Toolbar
Ctrl+ A: selects three Body Types: Solid, Surface, and Line
Ctrl+ B: equivalent to Selection Filter: Bodies (also accessible via the Selection Toolbar)
Ctrl+ C: equivalent to Copy (Sketching mode only; also accessible via the Modify Toolbox)
Ctrl+ E: equivalent to Selection Filter: Edges (also accessible via the Selection Toolbar)
Ctrl+ F: equivalent to Selection Filter: Faces (also accessible via the Selection Toolbar)
Ctrl+ N: equivalent to Start Over option (also accessible via the File Menu)
Ctrl+ O: equivalent to Load DesignModeler Database option (also accessible via the File Menu)
Ctrl+ P: equivalent to Selection Filter: Points (also accessible via the Selection Toolbar)
Ctrl+ S: equivalent to Save Project option (also accessible via the File Menu)
Ctrl+ V: equivalent to Paste (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ X: equivalent to Cut (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ Y: equivalent to Redo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ Z: equivalent to Undo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ +: equivalent to Expand Face Selection (also accessible via the Selection Toolbar and context menu)
Ctrl+ -: equivalent to Shrink Face Selection (also accessible via the Selection Toolbar and context menu)
F1: ANSYS Inc. online help with DesignModeler highlighted; for more information, see Help Menu
F2: Install help
F3: Apply (during feature creation; for more information, see Apply/Cancel in Plane)
F4: Cancel (during feature creation; for more information, see Apply/Cancel in Plane)
F5: equivalent to Generate (also accessible via the 3D Features toolbar)
F6: equivalent to Shaded Exterior and Edges, Shaded Exterior, and Wireframe model appearance controls (toggle between three; also accessible via the View Menu)
F7: equivalent to Zoom to Fit (also accessible via the Rotation Modes Toolbar toolbar)

## Slide 30: Adaptive Meshing
Implement during Solution options
  Define subset of timesteps to check: less computation time
  Multiple criteria options: skewness, strain energy, bounding box
  Only remeshes when criteria is met and only in problem areas
Notes: Escape: equivalent to New Selection (if button is not grayed out; also accessible via the Selection Toolbar
Ctrl+ A: selects three Body Types: Solid, Surface, and Line
Ctrl+ B: equivalent to Selection Filter: Bodies (also accessible via the Selection Toolbar)
Ctrl+ C: equivalent to Copy (Sketching mode only; also accessible via the Modify Toolbox)
Ctrl+ E: equivalent to Selection Filter: Edges (also accessible via the Selection Toolbar)
Ctrl+ F: equivalent to Selection Filter: Faces (also accessible via the Selection Toolbar)
Ctrl+ N: equivalent to Start Over option (also accessible via the File Menu)
Ctrl+ O: equivalent to Load DesignModeler Database option (also accessible via the File Menu)
Ctrl+ P: equivalent to Selection Filter: Points (also accessible via the Selection Toolbar)
Ctrl+ S: equivalent to Save Project option (also accessible via the File Menu)
Ctrl+ V: equivalent to Paste (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ X: equivalent to Cut (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ Y: equivalent to Redo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ Z: equivalent to Undo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ +: equivalent to Expand Face Selection (also accessible via the Selection Toolbar and context menu)
Ctrl+ -: equivalent to Shrink Face Selection (also accessible via the Selection Toolbar and context menu)
F1: ANSYS Inc. online help with DesignModeler highlighted; for more information, see Help Menu
F2: Install help
F3: Apply (during feature creation; for more information, see Apply/Cancel in Plane)
F4: Cancel (during feature creation; for more information, see Apply/Cancel in Plane)
F5: equivalent to Generate (also accessible via the 3D Features toolbar)
F6: equivalent to Shaded Exterior and Edges, Shaded Exterior, and Wireframe model appearance controls (toggle between three; also accessible via the View Menu)
F7: equivalent to Zoom to Fit (also accessible via the Rotation Modes Toolbar toolbar)

## Slide 31: Adaptive Mesh: Limitations
Must use linear tetrahedral elements for 3D bodies
  SOLID285’s
Scope to solid bodies or elements only – no shells
Altered mesh cannot be shared between linked analyses
No explicit indication where a remesh has occurred
May introduce solution chatter that would otherwise not be present
Notes: Escape: equivalent to New Selection (if button is not grayed out; also accessible via the Selection Toolbar
Ctrl+ A: selects three Body Types: Solid, Surface, and Line
Ctrl+ B: equivalent to Selection Filter: Bodies (also accessible via the Selection Toolbar)
Ctrl+ C: equivalent to Copy (Sketching mode only; also accessible via the Modify Toolbox)
Ctrl+ E: equivalent to Selection Filter: Edges (also accessible via the Selection Toolbar)
Ctrl+ F: equivalent to Selection Filter: Faces (also accessible via the Selection Toolbar)
Ctrl+ N: equivalent to Start Over option (also accessible via the File Menu)
Ctrl+ O: equivalent to Load DesignModeler Database option (also accessible via the File Menu)
Ctrl+ P: equivalent to Selection Filter: Points (also accessible via the Selection Toolbar)
Ctrl+ S: equivalent to Save Project option (also accessible via the File Menu)
Ctrl+ V: equivalent to Paste (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ X: equivalent to Cut (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ Y: equivalent to Redo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ Z: equivalent to Undo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ +: equivalent to Expand Face Selection (also accessible via the Selection Toolbar and context menu)
Ctrl+ -: equivalent to Shrink Face Selection (also accessible via the Selection Toolbar and context menu)
F1: ANSYS Inc. online help with DesignModeler highlighted; for more information, see Help Menu
F2: Install help
F3: Apply (during feature creation; for more information, see Apply/Cancel in Plane)
F4: Cancel (during feature creation; for more information, see Apply/Cancel in Plane)
F5: equivalent to Generate (also accessible via the 3D Features toolbar)
F6: equivalent to Shaded Exterior and Edges, Shaded Exterior, and Wireframe model appearance controls (toggle between three; also accessible via the View Menu)
F7: equivalent to Zoom to Fit (also accessible via the Rotation Modes Toolbar toolbar)

## Slide 32: Adaptive Mesh: Limitations
Cannot be used in combination with the following features/conditions on the same part:
Cyclic Symmetry
Contact Formulations: Normal Lagrange (3D), MPC, and Beam
Contact Behaviors: Auto Asymmetric
Point Mass, Beam Connection, Joints, Spring, and Bearing
Remote Force, Remote Displacement, Moment, Thermal Condition, and Remote Point
Spatially varying boundary conditions
Coupling
Constraint Equation
From ANSYS V16 Release Notes
Notes: Escape: equivalent to New Selection (if button is not grayed out; also accessible via the Selection Toolbar
Ctrl+ A: selects three Body Types: Solid, Surface, and Line
Ctrl+ B: equivalent to Selection Filter: Bodies (also accessible via the Selection Toolbar)
Ctrl+ C: equivalent to Copy (Sketching mode only; also accessible via the Modify Toolbox)
Ctrl+ E: equivalent to Selection Filter: Edges (also accessible via the Selection Toolbar)
Ctrl+ F: equivalent to Selection Filter: Faces (also accessible via the Selection Toolbar)
Ctrl+ N: equivalent to Start Over option (also accessible via the File Menu)
Ctrl+ O: equivalent to Load DesignModeler Database option (also accessible via the File Menu)
Ctrl+ P: equivalent to Selection Filter: Points (also accessible via the Selection Toolbar)
Ctrl+ S: equivalent to Save Project option (also accessible via the File Menu)
Ctrl+ V: equivalent to Paste (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ X: equivalent to Cut (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ Y: equivalent to Redo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ Z: equivalent to Undo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ +: equivalent to Expand Face Selection (also accessible via the Selection Toolbar and context menu)
Ctrl+ -: equivalent to Shrink Face Selection (also accessible via the Selection Toolbar and context menu)
F1: ANSYS Inc. online help with DesignModeler highlighted; for more information, see Help Menu
F2: Install help
F3: Apply (during feature creation; for more information, see Apply/Cancel in Plane)
F4: Cancel (during feature creation; for more information, see Apply/Cancel in Plane)
F5: equivalent to Generate (also accessible via the 3D Features toolbar)
F6: equivalent to Shaded Exterior and Edges, Shaded Exterior, and Wireframe model appearance controls (toggle between three; also accessible via the View Menu)
F7: equivalent to Zoom to Fit (also accessible via the Rotation Modes Toolbar toolbar)

## Slide 33: Adaptive Meshing: Procedure
For 3D bodies, you must set the mesh to linear tetrahedral:
Insert->Method->Definition->Method->Tetrahedrons
Insert->Method->Definition->Method->Element Midside Nodes->“Dropped”
Large Deflection must be turned on:
Analysis Settings->Solver Controls->Large Deflection-> On
Store Results At All Time Points:
Analysis Settings->Output Controls->Store Results At-> All Time Points
It may also be helpful to define more loading substeps to check at more points before the elements distort too far
Notes: Escape: equivalent to New Selection (if button is not grayed out; also accessible via the Selection Toolbar
Ctrl+ A: selects three Body Types: Solid, Surface, and Line
Ctrl+ B: equivalent to Selection Filter: Bodies (also accessible via the Selection Toolbar)
Ctrl+ C: equivalent to Copy (Sketching mode only; also accessible via the Modify Toolbox)
Ctrl+ E: equivalent to Selection Filter: Edges (also accessible via the Selection Toolbar)
Ctrl+ F: equivalent to Selection Filter: Faces (also accessible via the Selection Toolbar)
Ctrl+ N: equivalent to Start Over option (also accessible via the File Menu)
Ctrl+ O: equivalent to Load DesignModeler Database option (also accessible via the File Menu)
Ctrl+ P: equivalent to Selection Filter: Points (also accessible via the Selection Toolbar)
Ctrl+ S: equivalent to Save Project option (also accessible via the File Menu)
Ctrl+ V: equivalent to Paste (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ X: equivalent to Cut (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ Y: equivalent to Redo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ Z: equivalent to Undo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ +: equivalent to Expand Face Selection (also accessible via the Selection Toolbar and context menu)
Ctrl+ -: equivalent to Shrink Face Selection (also accessible via the Selection Toolbar and context menu)
F1: ANSYS Inc. online help with DesignModeler highlighted; for more information, see Help Menu
F2: Install help
F3: Apply (during feature creation; for more information, see Apply/Cancel in Plane)
F4: Cancel (during feature creation; for more information, see Apply/Cancel in Plane)
F5: equivalent to Generate (also accessible via the 3D Features toolbar)
F6: equivalent to Shaded Exterior and Edges, Shaded Exterior, and Wireframe model appearance controls (toggle between three; also accessible via the View Menu)
F7: equivalent to Zoom to Fit (also accessible via the Rotation Modes Toolbar toolbar)

## Slide 34: Adaptive Meshing: Procedure
With environment selected in the tree, insert Nonlinear Adaptive Region or select it from the Conditions toolbar
Can only be scoped to a body or named selection of elements
Select criterion and time range to check upon
Notes: Escape: equivalent to New Selection (if button is not grayed out; also accessible via the Selection Toolbar
Ctrl+ A: selects three Body Types: Solid, Surface, and Line
Ctrl+ B: equivalent to Selection Filter: Bodies (also accessible via the Selection Toolbar)
Ctrl+ C: equivalent to Copy (Sketching mode only; also accessible via the Modify Toolbox)
Ctrl+ E: equivalent to Selection Filter: Edges (also accessible via the Selection Toolbar)
Ctrl+ F: equivalent to Selection Filter: Faces (also accessible via the Selection Toolbar)
Ctrl+ N: equivalent to Start Over option (also accessible via the File Menu)
Ctrl+ O: equivalent to Load DesignModeler Database option (also accessible via the File Menu)
Ctrl+ P: equivalent to Selection Filter: Points (also accessible via the Selection Toolbar)
Ctrl+ S: equivalent to Save Project option (also accessible via the File Menu)
Ctrl+ V: equivalent to Paste (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ X: equivalent to Cut (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ Y: equivalent to Redo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ Z: equivalent to Undo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ +: equivalent to Expand Face Selection (also accessible via the Selection Toolbar and context menu)
Ctrl+ -: equivalent to Shrink Face Selection (also accessible via the Selection Toolbar and context menu)
F1: ANSYS Inc. online help with DesignModeler highlighted; for more information, see Help Menu
F2: Install help
F3: Apply (during feature creation; for more information, see Apply/Cancel in Plane)
F4: Cancel (during feature creation; for more information, see Apply/Cancel in Plane)
F5: equivalent to Generate (also accessible via the 3D Features toolbar)
F6: equivalent to Shaded Exterior and Edges, Shaded Exterior, and Wireframe model appearance controls (toggle between three; also accessible via the View Menu)
F7: equivalent to Zoom to Fit (also accessible via the Rotation Modes Toolbar toolbar)

## Slide 35
Check force/displacement convergence graphs or tabular data to find which time step/substep a remesh was applied
Adaptive Meshing: Results
Notes: Escape: equivalent to New Selection (if button is not grayed out; also accessible via the Selection Toolbar
Ctrl+ A: selects three Body Types: Solid, Surface, and Line
Ctrl+ B: equivalent to Selection Filter: Bodies (also accessible via the Selection Toolbar)
Ctrl+ C: equivalent to Copy (Sketching mode only; also accessible via the Modify Toolbox)
Ctrl+ E: equivalent to Selection Filter: Edges (also accessible via the Selection Toolbar)
Ctrl+ F: equivalent to Selection Filter: Faces (also accessible via the Selection Toolbar)
Ctrl+ N: equivalent to Start Over option (also accessible via the File Menu)
Ctrl+ O: equivalent to Load DesignModeler Database option (also accessible via the File Menu)
Ctrl+ P: equivalent to Selection Filter: Points (also accessible via the Selection Toolbar)
Ctrl+ S: equivalent to Save Project option (also accessible via the File Menu)
Ctrl+ V: equivalent to Paste (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ X: equivalent to Cut (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ Y: equivalent to Redo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ Z: equivalent to Undo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ +: equivalent to Expand Face Selection (also accessible via the Selection Toolbar and context menu)
Ctrl+ -: equivalent to Shrink Face Selection (also accessible via the Selection Toolbar and context menu)
F1: ANSYS Inc. online help with DesignModeler highlighted; for more information, see Help Menu
F2: Install help
F3: Apply (during feature creation; for more information, see Apply/Cancel in Plane)
F4: Cancel (during feature creation; for more information, see Apply/Cancel in Plane)
F5: equivalent to Generate (also accessible via the 3D Features toolbar)
F6: equivalent to Shaded Exterior and Edges, Shaded Exterior, and Wireframe model appearance controls (toggle between three; also accessible via the View Menu)
F7: equivalent to Zoom to Fit (also accessible via the Rotation Modes Toolbar toolbar)

## Slide 36
Compare pre-mesh change and post-mesh change substeps to find regions of improvement
Adaptive Meshing: Results
Notes: Escape: equivalent to New Selection (if button is not grayed out; also accessible via the Selection Toolbar
Ctrl+ A: selects three Body Types: Solid, Surface, and Line
Ctrl+ B: equivalent to Selection Filter: Bodies (also accessible via the Selection Toolbar)
Ctrl+ C: equivalent to Copy (Sketching mode only; also accessible via the Modify Toolbox)
Ctrl+ E: equivalent to Selection Filter: Edges (also accessible via the Selection Toolbar)
Ctrl+ F: equivalent to Selection Filter: Faces (also accessible via the Selection Toolbar)
Ctrl+ N: equivalent to Start Over option (also accessible via the File Menu)
Ctrl+ O: equivalent to Load DesignModeler Database option (also accessible via the File Menu)
Ctrl+ P: equivalent to Selection Filter: Points (also accessible via the Selection Toolbar)
Ctrl+ S: equivalent to Save Project option (also accessible via the File Menu)
Ctrl+ V: equivalent to Paste (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ X: equivalent to Cut (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ Y: equivalent to Redo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ Z: equivalent to Undo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ +: equivalent to Expand Face Selection (also accessible via the Selection Toolbar and context menu)
Ctrl+ -: equivalent to Shrink Face Selection (also accessible via the Selection Toolbar and context menu)
F1: ANSYS Inc. online help with DesignModeler highlighted; for more information, see Help Menu
F2: Install help
F3: Apply (during feature creation; for more information, see Apply/Cancel in Plane)
F4: Cancel (during feature creation; for more information, see Apply/Cancel in Plane)
F5: equivalent to Generate (also accessible via the 3D Features toolbar)
F6: equivalent to Shaded Exterior and Edges, Shaded Exterior, and Wireframe model appearance controls (toggle between three; also accessible via the View Menu)
F7: equivalent to Zoom to Fit (also accessible via the Rotation Modes Toolbar toolbar)

## Slide 37: Meshing misc.
Fixed Size Function For Sheets – set all surface bodies to same mesh density
Face Meshing can be done without mapping– fewer elements in noncritical bodies attached to critical ones
Tetra/Pyramid Free Mesh Type – give bodies a pyramidal surface, tetrahedral core mesh
Vertex alignment options available in MultiZone meshing – previously only in face meshing
Inflation allowed for 2D mapped surfaces
Can now sweep across multiple parts or named selections, and define sweep element size with numerical argument or edge reference

## Slide 38: Weld Connections

## Slide 39: Weld Connections
ANSYS has started to implement welds in DM
Two types of weld: Continuous and Skip (beta feature)
Project->Surface Extension

## Slide 40: Weld Connections

## Slide 41: Weld Connections
Limitations
  Only works on perpendicular surfaces
  Only works in DM
  Watch out for partial welds (see picture below)

## Slide 42: Contacts misc
Contact smoothing for more accurate circular/cylindrical/spherical contact regions – contact is mapped based on geometry, not mesh
Element orientation (bodies only)
Bolt tool probes results for all pretensions
Contact results report far contact fields as undefined rather than zero
V15
V16

## Slide 43: Spaceclaim

## Slide 44: Spaceclaim
Community usage?
Can now read DM files
Yes—you do need a separate license to run it
User friendly, terrific user experience after learning
Similar to Solidworks in feel
No design tree! Able to make changes without corrupting the rest of the model!

## Slide 45: Material Modeling Improvements

## Slide 46: Composites
Better tree structure
Imperfection modeling
More individual ply control
  Fiber direction
  Ply stresses
From ANSYS V16 Release Notes

## Slide 47: Inclined Crack Modeling
Crack coordinate system created for each crack
More crack definition features to work with new crack coordinate system
From ANSYS V16 Release Notes
From ANSYS V16 Release Notes

## Slide 48: V15 - Reminders
Notes: Escape: equivalent to New Selection (if button is not grayed out; also accessible via the Selection Toolbar
Ctrl+ A: selects three Body Types: Solid, Surface, and Line
Ctrl+ B: equivalent to Selection Filter: Bodies (also accessible via the Selection Toolbar)
Ctrl+ C: equivalent to Copy (Sketching mode only; also accessible via the Modify Toolbox)
Ctrl+ E: equivalent to Selection Filter: Edges (also accessible via the Selection Toolbar)
Ctrl+ F: equivalent to Selection Filter: Faces (also accessible via the Selection Toolbar)
Ctrl+ N: equivalent to Start Over option (also accessible via the File Menu)
Ctrl+ O: equivalent to Load DesignModeler Database option (also accessible via the File Menu)
Ctrl+ P: equivalent to Selection Filter: Points (also accessible via the Selection Toolbar)
Ctrl+ S: equivalent to Save Project option (also accessible via the File Menu)
Ctrl+ V: equivalent to Paste (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ X: equivalent to Cut (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ Y: equivalent to Redo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ Z: equivalent to Undo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ +: equivalent to Expand Face Selection (also accessible via the Selection Toolbar and context menu)
Ctrl+ -: equivalent to Shrink Face Selection (also accessible via the Selection Toolbar and context menu)
F1: ANSYS Inc. online help with DesignModeler highlighted; for more information, see Help Menu
F2: Install help
F3: Apply (during feature creation; for more information, see Apply/Cancel in Plane)
F4: Cancel (during feature creation; for more information, see Apply/Cancel in Plane)
F5: equivalent to Generate (also accessible via the 3D Features toolbar)
F6: equivalent to Shaded Exterior and Edges, Shaded Exterior, and Wireframe model appearance controls (toggle between three; also accessible via the View Menu)
F7: equivalent to Zoom to Fit (also accessible via the Rotation Modes Toolbar toolbar)

## Slide 49: Preprocessing
Promote a scoping to a named selection!
  Consider making named selections the norm /best practice
  For those who don't plan well...
New mapping processor
  Can map stress/strain data from text file onto nodes
  UV mapping algorithm (surfaces don't have to be coincident)
    Projects data onto surface
    Eases mapping from deformed to unreformed shapes!

## Slide 50: Meshing
Local Min-Size meshing
  Overrides min-size in advance meshing (proximity and/or curvature)
Mesh failures are color coded / highlighted by white axes
Images from help manual

## Slide 51: Solver Improvements
GPU added to solve process settings / GUI
  Can have 1 GPU on SMP using Sparse now
New Arc-length methodology
  Now based on “Crisfield“ theory
  Less likely to retrace own steps backward
  Supposed to do better with plasticity
NROPT,UNSYM exposed in WB
  Can aid help with non-convergence/unstable problems
  More expensive computationally (30% on solve time?)
  Can use the WB/Mechanical generated springs
Sparse has better (um, different) detection/handling of singular matrices.
  PIVCHECK command can be disabled.

## Slide 52: Contact Debonding
Contact Debonding!
  CZM technology
  Uses CONT17X
  Define material model
Interface Delamination
  uses INT20X elements
  more complex separation functions
Notes: Escape: equivalent to New Selection (if button is not grayed out; also accessible via the Selection Toolbar
Ctrl+ A: selects three Body Types: Solid, Surface, and Line
Ctrl+ B: equivalent to Selection Filter: Bodies (also accessible via the Selection Toolbar)
Ctrl+ C: equivalent to Copy (Sketching mode only; also accessible via the Modify Toolbox)
Ctrl+ E: equivalent to Selection Filter: Edges (also accessible via the Selection Toolbar)
Ctrl+ F: equivalent to Selection Filter: Faces (also accessible via the Selection Toolbar)
Ctrl+ N: equivalent to Start Over option (also accessible via the File Menu)
Ctrl+ O: equivalent to Load DesignModeler Database option (also accessible via the File Menu)
Ctrl+ P: equivalent to Selection Filter: Points (also accessible via the Selection Toolbar)
Ctrl+ S: equivalent to Save Project option (also accessible via the File Menu)
Ctrl+ V: equivalent to Paste (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ X: equivalent to Cut (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ Y: equivalent to Redo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ Z: equivalent to Undo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ +: equivalent to Expand Face Selection (also accessible via the Selection Toolbar and context menu)
Ctrl+ -: equivalent to Shrink Face Selection (also accessible via the Selection Toolbar and context menu)
F1: ANSYS Inc. online help with DesignModeler highlighted; for more information, see Help Menu
F2: Install help
F3: Apply (during feature creation; for more information, see Apply/Cancel in Plane)
F4: Cancel (during feature creation; for more information, see Apply/Cancel in Plane)
F5: equivalent to Generate (also accessible via the 3D Features toolbar)
F6: equivalent to Shaded Exterior and Edges, Shaded Exterior, and Wireframe model appearance controls (toggle between three; also accessible via the View Menu)
F7: equivalent to Zoom to Fit (also accessible via the Rotation Modes Toolbar toolbar)

## Slide 53: More Contact
MAPDL Contact -- user-programmable definitions
  Stiffness based on frequency, nonlinear, etc.
FTOLN now affects FKN!
Contact surface wearing
  “Archard” wear model (or user defined subroutine)
  Moves contact node by depth of calculated wear
    Controlled via material property, TB, WEAR
  Total wear stored in NMISC data
Notes: Escape: equivalent to New Selection (if button is not grayed out; also accessible via the Selection Toolbar
Ctrl+ A: selects three Body Types: Solid, Surface, and Line
Ctrl+ B: equivalent to Selection Filter: Bodies (also accessible via the Selection Toolbar)
Ctrl+ C: equivalent to Copy (Sketching mode only; also accessible via the Modify Toolbox)
Ctrl+ E: equivalent to Selection Filter: Edges (also accessible via the Selection Toolbar)
Ctrl+ F: equivalent to Selection Filter: Faces (also accessible via the Selection Toolbar)
Ctrl+ N: equivalent to Start Over option (also accessible via the File Menu)
Ctrl+ O: equivalent to Load DesignModeler Database option (also accessible via the File Menu)
Ctrl+ P: equivalent to Selection Filter: Points (also accessible via the Selection Toolbar)
Ctrl+ S: equivalent to Save Project option (also accessible via the File Menu)
Ctrl+ V: equivalent to Paste (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ X: equivalent to Cut (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ Y: equivalent to Redo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ Z: equivalent to Undo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ +: equivalent to Expand Face Selection (also accessible via the Selection Toolbar and context menu)
Ctrl+ -: equivalent to Shrink Face Selection (also accessible via the Selection Toolbar and context menu)
F1: ANSYS Inc. online help with DesignModeler highlighted; for more information, see Help Menu
F2: Install help
F3: Apply (during feature creation; for more information, see Apply/Cancel in Plane)
F4: Cancel (during feature creation; for more information, see Apply/Cancel in Plane)
F5: equivalent to Generate (also accessible via the 3D Features toolbar)
F6: equivalent to Shaded Exterior and Edges, Shaded Exterior, and Wireframe model appearance controls (toggle between three; also accessible via the View Menu)
F7: equivalent to Zoom to Fit (also accessible via the Rotation Modes Toolbar toolbar)

## Slide 54: Contact
Bolt thread modeling
  Need to have a refined mesh
  Specify bolt axis/CS
  Enter Pitch, Thread Angle, Diameter, etc.
Image from help manual
Notes: Escape: equivalent to New Selection (if button is not grayed out; also accessible via the Selection Toolbar
Ctrl+ A: selects three Body Types: Solid, Surface, and Line
Ctrl+ B: equivalent to Selection Filter: Bodies (also accessible via the Selection Toolbar)
Ctrl+ C: equivalent to Copy (Sketching mode only; also accessible via the Modify Toolbox)
Ctrl+ E: equivalent to Selection Filter: Edges (also accessible via the Selection Toolbar)
Ctrl+ F: equivalent to Selection Filter: Faces (also accessible via the Selection Toolbar)
Ctrl+ N: equivalent to Start Over option (also accessible via the File Menu)
Ctrl+ O: equivalent to Load DesignModeler Database option (also accessible via the File Menu)
Ctrl+ P: equivalent to Selection Filter: Points (also accessible via the Selection Toolbar)
Ctrl+ S: equivalent to Save Project option (also accessible via the File Menu)
Ctrl+ V: equivalent to Paste (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ X: equivalent to Cut (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ Y: equivalent to Redo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ Z: equivalent to Undo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ +: equivalent to Expand Face Selection (also accessible via the Selection Toolbar and context menu)
Ctrl+ -: equivalent to Shrink Face Selection (also accessible via the Selection Toolbar and context menu)
F1: ANSYS Inc. online help with DesignModeler highlighted; for more information, see Help Menu
F2: Install help
F3: Apply (during feature creation; for more information, see Apply/Cancel in Plane)
F4: Cancel (during feature creation; for more information, see Apply/Cancel in Plane)
F5: equivalent to Generate (also accessible via the 3D Features toolbar)
F6: equivalent to Shaded Exterior and Edges, Shaded Exterior, and Wireframe model appearance controls (toggle between three; also accessible via the View Menu)
F7: equivalent to Zoom to Fit (also accessible via the Rotation Modes Toolbar toolbar)

## Slide 55: Shell to Solid Submodels
3D shell model to 3D solid model
  In “Transfer Key” specify Shell-Solid
    Imported Loads detail window
  As with most submodels, beware the rotating nodes CS’s
  UY mapped for nodes within center region (20% the thickness)…
    Beware over/under constraint here.
    Ideally this would be a single set of nodes
Image from help manual
Notes: Escape: equivalent to New Selection (if button is not grayed out; also accessible via the Selection Toolbar
Ctrl+ A: selects three Body Types: Solid, Surface, and Line
Ctrl+ B: equivalent to Selection Filter: Bodies (also accessible via the Selection Toolbar)
Ctrl+ C: equivalent to Copy (Sketching mode only; also accessible via the Modify Toolbox)
Ctrl+ E: equivalent to Selection Filter: Edges (also accessible via the Selection Toolbar)
Ctrl+ F: equivalent to Selection Filter: Faces (also accessible via the Selection Toolbar)
Ctrl+ N: equivalent to Start Over option (also accessible via the File Menu)
Ctrl+ O: equivalent to Load DesignModeler Database option (also accessible via the File Menu)
Ctrl+ P: equivalent to Selection Filter: Points (also accessible via the Selection Toolbar)
Ctrl+ S: equivalent to Save Project option (also accessible via the File Menu)
Ctrl+ V: equivalent to Paste (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ X: equivalent to Cut (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ Y: equivalent to Redo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ Z: equivalent to Undo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ +: equivalent to Expand Face Selection (also accessible via the Selection Toolbar and context menu)
Ctrl+ -: equivalent to Shrink Face Selection (also accessible via the Selection Toolbar and context menu)
F1: ANSYS Inc. online help with DesignModeler highlighted; for more information, see Help Menu
F2: Install help
F3: Apply (during feature creation; for more information, see Apply/Cancel in Plane)
F4: Cancel (during feature creation; for more information, see Apply/Cancel in Plane)
F5: equivalent to Generate (also accessible via the 3D Features toolbar)
F6: equivalent to Shaded Exterior and Edges, Shaded Exterior, and Wireframe model appearance controls (toggle between three; also accessible via the View Menu)
F7: equivalent to Zoom to Fit (also accessible via the Rotation Modes Toolbar toolbar)

## Slide 56: Automatic Rezoning
Manual Rezoning fully implemented in MAPDL
  Writes deformed nodes
  Makes facets/geometry in the deformed shape
  Meshes new volume/area
  Transfer displacements from previous analysis
  Resolves -- Lather, rinse, repeat…
Automatic Rezoning just splits the element edges
  a.k.a. “Mesh Nonlinear Adaptivity”
  An EREFINE essentially.
  Manual is pretty clear this won’t help element shape distortion errors… yet.
Notes: Escape: equivalent to New Selection (if button is not grayed out; also accessible via the Selection Toolbar
Ctrl+ A: selects three Body Types: Solid, Surface, and Line
Ctrl+ B: equivalent to Selection Filter: Bodies (also accessible via the Selection Toolbar)
Ctrl+ C: equivalent to Copy (Sketching mode only; also accessible via the Modify Toolbox)
Ctrl+ E: equivalent to Selection Filter: Edges (also accessible via the Selection Toolbar)
Ctrl+ F: equivalent to Selection Filter: Faces (also accessible via the Selection Toolbar)
Ctrl+ N: equivalent to Start Over option (also accessible via the File Menu)
Ctrl+ O: equivalent to Load DesignModeler Database option (also accessible via the File Menu)
Ctrl+ P: equivalent to Selection Filter: Points (also accessible via the Selection Toolbar)
Ctrl+ S: equivalent to Save Project option (also accessible via the File Menu)
Ctrl+ V: equivalent to Paste (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ X: equivalent to Cut (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ Y: equivalent to Redo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ Z: equivalent to Undo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ +: equivalent to Expand Face Selection (also accessible via the Selection Toolbar and context menu)
Ctrl+ -: equivalent to Shrink Face Selection (also accessible via the Selection Toolbar and context menu)
F1: ANSYS Inc. online help with DesignModeler highlighted; for more information, see Help Menu
F2: Install help
F3: Apply (during feature creation; for more information, see Apply/Cancel in Plane)
F4: Cancel (during feature creation; for more information, see Apply/Cancel in Plane)
F5: equivalent to Generate (also accessible via the 3D Features toolbar)
F6: equivalent to Shaded Exterior and Edges, Shaded Exterior, and Wireframe model appearance controls (toggle between three; also accessible via the View Menu)
F7: equivalent to Zoom to Fit (also accessible via the Rotation Modes Toolbar toolbar)

## Slide 57: Shared Topology
Toggles on/off – if you don’t know about it, it’s a must read to avoid problems.
  Default is to execute behind the scenes on way to Mechanical
  Can be forced to earlier location in the tree
    And then hidden – so you won’t know that it is happening prior to other operations!
Face coloring by shared topology specification
  Not by success / actual connection
Specify face joints manually…
  Must be two parts within same body
  Can be done after shared topology operation
Notes: Escape: equivalent to New Selection (if button is not grayed out; also accessible via the Selection Toolbar
Ctrl+ A: selects three Body Types: Solid, Surface, and Line
Ctrl+ B: equivalent to Selection Filter: Bodies (also accessible via the Selection Toolbar)
Ctrl+ C: equivalent to Copy (Sketching mode only; also accessible via the Modify Toolbox)
Ctrl+ E: equivalent to Selection Filter: Edges (also accessible via the Selection Toolbar)
Ctrl+ F: equivalent to Selection Filter: Faces (also accessible via the Selection Toolbar)
Ctrl+ N: equivalent to Start Over option (also accessible via the File Menu)
Ctrl+ O: equivalent to Load DesignModeler Database option (also accessible via the File Menu)
Ctrl+ P: equivalent to Selection Filter: Points (also accessible via the Selection Toolbar)
Ctrl+ S: equivalent to Save Project option (also accessible via the File Menu)
Ctrl+ V: equivalent to Paste (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ X: equivalent to Cut (Sketching Mode only; also accessible via the Modify Toolbox)
Ctrl+ Y: equivalent to Redo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ Z: equivalent to Undo (Sketching Mode only; also accessible via the toolbar)
Ctrl+ +: equivalent to Expand Face Selection (also accessible via the Selection Toolbar and context menu)
Ctrl+ -: equivalent to Shrink Face Selection (also accessible via the Selection Toolbar and context menu)
F1: ANSYS Inc. online help with DesignModeler highlighted; for more information, see Help Menu
F2: Install help
F3: Apply (during feature creation; for more information, see Apply/Cancel in Plane)
F4: Cancel (during feature creation; for more information, see Apply/Cancel in Plane)
F5: equivalent to Generate (also accessible via the 3D Features toolbar)
F6: equivalent to Shaded Exterior and Edges, Shaded Exterior, and Wireframe model appearance controls (toggle between three; also accessible via the View Menu)
F7: equivalent to Zoom to Fit (also accessible via the Rotation Modes Toolbar toolbar)